## Slide 1: ROBOTINO PROJECT
Suraj Karki
19.09.2025
Prof. Dr.-Ing. Christian Schwede
Notes: HAW

## Slide 2
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Introduction
Robotino AGV → mobile robot for education & research
Equipped with sensors (SICK LMS100, optical encoders,
infrared sensor and camera) for autonomous navigation.
It has omnidirectional movement for flexible navigation.
Notes: HAW

## Slide 3
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 3
Problem statement
Current path networks for Robotino are manual and slow
Relies heavily on expert knowledge
Adapting paths to new or changing factory layouts is challenging and time-consuming.
Sensor noise and localization errors reduce accuracy and robustness
Notes: HAW

## Slide 4
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 4
objective
To generate a map of the environment including stations
To generate an optimized path network based on recordings
Notes: HAW

## Slide 5
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
SLAM (Simultaneous Localization and Mapping)
  It is the process for a mobile robot to build a map of the environment and use this map to compute its location simultaneously. 1
1. Bailey, Tim, and Hugh Durrant-Whyte. "Simultaneous localization and mapping (SLAM): Part II." IEEE robotics & automation magazine 13.3 (2006): 108-117.
Notes: HAW

## Slide 6
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Types of SLAM:
  Filtering
    State is estimated “on the go” with latest measurements
    For example, Kalman Filter, EKF, Particle Filtering, etc.
  Smoothing
    Full trajectories are estimated using complete set of measurements
    For example, Pose Graph Optimization
Notes: HAW

## Slide 7
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Workflow for Map Generation
Notes: HAW

## Slide 8
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Pose Graph
  A pose graph contains nodes connected by edges.
  Nodes → robot poses (position + orientation) at different times
  Edges → constraints between poses (from odometry,
  sensor measurements, loop closures)
  These edge constraints also represent the uncertainty
  associated with that measurement.
Notes: HAW

## Slide 9
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Loop Closure
  It tells the SLAM system that the robot has returned to a
  previously visited area.
  It helps to correct errors(drift in trajectory) in the map.
  Connecting two nodes that are not next to each other
  (non-sequential), creates a loop closure.
Notes: HAW

## Slide 10
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Pose Graph Optimization
  Goal: Move all the nodes so that the distances and directions between them match the measurements as closely as possible.
  Step 1: Represent Constraints Mathematically
Notes: HAW

## Slide 11
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Pose Graph Optimization
  Step 2: Formulate Optimization Problem
  Objective: Minimize total error between predicted and measured relative poses:
  Adjust node positions so all edges “fit” as well as possible
Notes: HAW

## Slide 12
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Pose Graph Optimization
  Step 3: Solve Nonlinear Least Squares
  Use optimization algorithms:
    Gauss-Newton
    Dogleg methods
  Iteratively adjust node poses until convergence.
Notes: HAW

## Slide 13
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Pose Graph Optimization
  Step 4: Correct Drift & Align Loops
  Sequential odometry errors are reduced
  Loop closures are enforced → trajectory is globally consistent
  Step 5: Result
  Optimized node poses → accurate robot trajectory
  Can be used to build high-quality maps (occupancy grids, point clouds)
Notes: HAW

## Slide 14
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Pose Graph Optimization
Notes: HAW

## Slide 15
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Occupancy Grid Map
  A way to represent the environment as a grid of cells.
  Each cell in the occupancy grid has a value representing the probability of the occupancy of that cell
  Value close to 1 → cell likely occupied (obstacle).
  Value close to 0 → cell likely free (no obstacle).
  Value = 0.5 → unknown
Notes: HAW

## Slide 16
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Occupancy Grid Map
Optimized Scans & Poses
2D Probability Occupancy Grid Map
Notes: HAW

## Slide 17
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Workflow for Optimized Path-Network Generation
Notes: HAW

## Slide 18
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Path Planning
  Finding a path from the current position to the goal position given a map of the environment.
Path Planning Algorithms
  Search-based: A*
  Sampling-based: RRT, RRT*
1. Bailey, Tim, and Hugh Durrant-Whyte. "Simultaneous localization and mapping (SLAM): Part II." IEEE robotics & automation magazine 13.3 (2006): 108-117.
Notes: HAW

## Slide 19
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
A*
  A popular graph traversal path planning algorithm.
  Heuristic-Based: Combines actual cost from the start with estimated cost to the goal.
  Evaluation function, f(n)=g(n)+h(n)
    Where,f(n) is the estimated total cost of the path through node n.
    g(n) is actual cost from the start node to n.
    h(n) is estimated cost (heuristic) from n to the goal node.
Notes: HAW

## Slide 20
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
A*
  Optimality: Guarantees the shortest path if the heuristic is admissible (never overestimates).
  Completeness: If a path exists, A* will always find it.
  The performance of A* depends heavily on the heuristic function chosen.
  Works with different heuristics like Manhattan distance, Euclidean distance, or custom heuristics depending on the problem.
Notes: HAW

## Slide 21
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Workings of A*
  Initialization
    Setting up two essential lists:
      “open” list: initialize with starting node
      “closed” list: begins empty
    Each node stores 4 critical information:
      g: The actual cost from the start node
      h: The estimated cost to the goal
      f: The sum of g and h
      parent: Reference to the previous node (for path reconstruction)
Notes: HAW

## Slide 22
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Workings of A*
  Main Loop:
    The main loop will continues until either:
      The goal is reached (success)
      The open list becomes empty (failure - no path exists)
    During each iteration, the algorithm:
      Selects the most promising node (lowest f value) from the open list
      Moves it to the closed list
      Examines all neighboring nodes
Notes: HAW

## Slide 23
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Workings of A*
  Neighbor Evaluation:
    For each neighbor, the algorithm:
      Skips nodes already in the closed list
      Calculates a tentative g score
      Updates node values if a better path is found
      Adds new nodes to the open list
Notes: HAW

## Slide 24
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Workings of A*
  Path reconstruction:
    Once the goal is reached, the algorithm works backward through the parent references to construct the optimal path from start to goal.
Notes: HAW

## Slide 25
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
RRT (Rapidly Exploring Random Tree)
  Sampling-based path planning algorithm
  Grows a random tree by sampling points in the space
  and connect them to the nearest existing node.
  Efficiently explores large, high-dimensional, or obstacle-filled environments.
  if a path exists, RRT will find it given enough time.
  basic RRT does not ensure the shortest path
Notes: HAW

## Slide 26
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Workings of RRT
  Define the State Space: Represent the environment (e.g., SE2 for 2D with orientation).
  Initialize the Tree – Start with the root node at the robot’s initial position.
Notes: HAW

## Slide 27
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Workings of RRT
  Random Sampling – Sample a random state Xrand​ within the state space.
Notes: HAW

## Slide 28
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Workings of RRT
  Find Nearest Node – Identify the tree node Xnear​ closest to Xrand​.
Notes: HAW

## Slide 29
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Workings of RRT
  ​Generate New Node – Extend from Xnear​ toward Xrand​ to create Xnew​, using feasible motion models.
Notes: HAW

## Slide 30
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Workings of RRT
  ​Collision Checking – Validate that the motion from Xnear​ to Xnew​ is collision-free.
Notes: HAW

## Slide 31
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Workings of RRT
  ​​ Add Node to Tree – If valid, add Xnew​ and connect it to Xnear.
Notes: HAW

## Slide 32
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Workings of RRT
  ​​ Iterate – Repeat steps 3–7 until the goal is reached or a stopping condition is met.
Notes: HAW

## Slide 33
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
Workings of RRT
  ​​ Path Extraction – Trace back through parent nodes to extract the path.
Notes: HAW

## Slide 34
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Methods & implementations
RRT*
  ​​ It expands the tree in a similar way like RRT.
  But it rewires the tree in a way, that a given search radius and always tries to find shorter path from the randomly sampled node back to the start in the tree.
Notes: HAW

## Slide 35
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
results
Generated Map of IOT Factory
Notes: HAW

## Slide 36
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
results
Generated Map of Warehouse
Notes: HAW

## Slide 37
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
results
Path Generated by RRT*
Notes: HAW

## Slide 38
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
results
Path Generated by A*
Notes: HAW

## Slide 39
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Critical reflection
Points
  subpoint
Notes: HAW

## Slide 40
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Notes: HAW

## Slide 41
Robotino Project | Hochschule Bielefeld | 19.09.2025 | Page 2
Notes: HAW